## Slide 1: Field and petrographic study of heterogeneous oil saturation in submarine channel and adjacent facies, Monterey Formation, Point Fermin, Palos Verdes, California.
By: Nawaf AlShammary
MARS meeting – Fall 2012
Thesis Committee Chair: Professor Richard J. Behl, CSULB
Thesis Committee Members: Donald D. Clarke
& Professor Tom Kelty, CSULB

## Slide 2
Nawaf AlShammary: Presenter’s Background
Education
Professional Experience
MSc, Geological Sciences, CSU Long Beach
( Fall 2010-May 2013)
BSc, Geophysics, minor Physics, University of New Orleans
(1996-2000)
Seismic Data Processing, Saudi Aramco (2001-2003)
Exploration school, Saudi Aramco and OGCI (2003)
Wellsite Operational Geologist, Saudi Aramco (2003-2008)
Wellsite Development, Saudi Aramco (2008-2010)

## Slide 3: Location

## Slide 4: Los Angeles Basin
Study area

## Slide 5: Stratigraphy & Lithofacies
Monterey Formation in Palos Verdes
  Malaga Mudstone
  Valmonte Diatomite
  Altamira Shale
Altamira Shale
  Phosphatic lithofacies
  Cherty lithofacies
  Tuffaceous lithofacies

## Slide 6: Point Fermin
  The Altamira Shale (tuffaceous lithofacies)
    Hemipelagic sediments
  Point Fermin Sandstone
    Submarine channel sediments

## Slide 7: Contact between the two units
(californiacoastline.org)
N

## Slide 8: Channel Margin Contact

## Slide 9: Sandstone beds in Altamira Shale

## Slide 10
Behl (2012)

## Slide 11: Point Fermin Sandstone facies
Schist and phosphatic breccia scoured
down through sandstone to cohesive shale bed
Dish structures in coarse-grained sandstone
Behl (2012)

## Slide 12: Previous Work
Spotts (1964)
  Current flow direction in the submarine channel
    Imbricated clasts and sedimentary structures
  Source – southeast
Russell (1987)
  Stratigraphic and sedimentologic paper on the submarine deposits.
    Little emphasis on the Altamira Shale deposits
    Concluded – North source based on sedimentary structures

## Slide 13: Biostratigraphy
Sloan (1987)
  Radiolarians in Point Fermin fan deposits
    between 11.4–12.7 Ma

## Slide 14: Petrography
Cherven and Russell (1987)
  Petrographic study and comparison between the Point Fermin Sandstone (6 samples) and Beta Oil Field (1 sample)
  Beta field is quartzofeldspathic arenite
  Point Fermin is a lithic arenite
Spotts (1966)
  Dolomite at Point Fermin was of
  organic origin

## Slide 15: Research Objectives
Understand the lateral and vertical heterogeneity in hydrocarbon saturation in closely associated sandstones at Point Fermin
Compare the petrology of sandstone samples from the Point Fermin Sandstone and the adjacent Altamira Shale facies
Examine and explain porosity and permeability differences between the two units
Create a map to show the stratigraphic architecture

## Slide 16: Hypothesis
The sandstone is distinct enough in porosity and permeability between the units to influence charge
  This is due to distinct depositional environment and processes that made different grain size, sorting and diagenesis
  This is due to provenance differences between the Altamira Shale and the Point Fermin Sandstone, that resulted in different grain composition and diagenesis
or

## Slide 17: Methods
Field measurement and sampling
Petrographic analysis
  Gazzi-Dickinson method (300 points)
  Best for provenance studies
  50 – 60 samples
Measurement of reservoir properties by a commercial laboratory
  Porosity, permeability, and HC saturation, etc
XRD and SEM with EDS/XRF
  provide details about composition and grains sufrace
Detailed map of the stratigraphic architecture of the outcrop
  LiDAR

## Slide 18: Initial Work: GIS spatial analysis
Grain size
(1-fine, 3- medium, 5- coarse)
Sandstone
%

## Slide 19: Pilot data analysis
6 samples were taken
  3 from Altamira Shale sandstones
  3 from Point Fermin sandstones
Samples sent to Core Lab for conventional core analysis
  Permeability, porosity, fluid saturation, grain density, humidity and V-clay.
Made thin sections and study them petrographically
  Images, analysis, point counting
XRD and SEM with EDS/XRF

## Slide 20: Altamira Shale samples
AS-01
AS-02
AS-03

## Slide 21: Point Fermin samples
PF-104
PF-105
PF-106

## Slide 22: Oil saturation on outcrop
AS-01
PF-105

## Slide 23: Metamorphic provenance
AS-01
PF-106
Point Fermin
Altamira Shale

## Slide 24: Porosity %
Chart: 
| Altamira Shale | Point Fermin
Series 1 | 19.3 | 25.3
Series 2 | 4.6 | 40.9
Series 3 | 31.7 | 27.3

## Slide 25: Petrographic porosity analysis
Chart: 
| AS-01 | AS-02 | AS-03 | PF-104 | PF-105 | PF-106
Intergranular Ø | 20 | 100 | 0 | 30 | 40 | 25
Intragranular Ø | 80 | 0 | 25 | 0 | 0 | 5
Fracture Ø | 0 | 0 | 75 | 70 | 60 | 70
* Handling induced
fractures

## Slide 26: Altamira Shale
Perm: 0.024 md
Porosity: 19.3 %
Oil Saturation: 5.7%
Total fluid saturation:
54.4%
AS-01

## Slide 27: AS-02
Perm.: 0.006 md
Porosity: 4.6%
Oil Satur.: 24.3%
Tot. Fluid Satur.: 81.5%
Altamira
Shale

## Slide 28
Altamira Shale
epoxy
epoxy
Dolomite crystal

## Slide 29: Oil
PF-104
PF-105
Perm.: 67.6 md
Porosity: 24.3%
Oil Satur.: 4.2%
Tot. Fluid Satur.:43.9%
Perm.: 202.2 md
Porosity: 40.9%
Oil Satur.: 20.3%
Tot. Fluid Satur.:35.1%
Point Fermin
Oil
epoxy
Oil

## Slide 30: Dolomite cementation crystals with oil nuclei
Pf-104
PF-106
Pf-104
Point Fermin

## Slide 31: Local intracrystaline porosity in cement
PF-106
PF-106
Point Fermin

## Slide 32: Intragranular porosity in lithic grains
AS-01
AS-01
PF-106
Altamira Shale & Point Fermin

## Slide 33: % Oil / Volume Rock
Chart: 
| Oil | Rock
AS-01 | 1.1 | 98.8
Chart: 
| Oil | Rock
AS-02 | 1.12 | 98.88
Chart: AS-03
| Oil | Rock
AS-03 | 0 | 100
Chart: 
| Oil | Rock
PF-104 | 1.06 | 98.94
Chart: 
| Oil | Rock
PF-105 | 8.3 | 91.7
Chart: 
| Oil | Rock
PF-106 | 3.58 | 96.42

## Slide 34: Preliminary Conclusions
Both units have same metamorphic provenance
Significant intragranular porosity in some sandstones
Evidence of early cementation of Altamira Shale sandstones
Depositional and diagenetic environment controlling time of cementation was critical to differences in oil saturation, rather than grain composition or texture

## Slide 35: Importance
Importance of the provenance for the sandstone oil reservoirs
Understanding stratigraphic traps
The diagenesis and its effect on oil saturation
Difference in porosity types and its connection to oil saturation

## Slide 36: Thank you and appreciate your comments

## Slide 37: References
Behl, R.J., and Morita, S., 2007, The Monterey Formation of the Palos Verdes Hills, California: stratigraphy and diagenetic implications for burial and uplift history: in Brown, A.R., Shlemon, R.J., and Cooper, J.D., eds., Geology and Paleontology of the Palos Verdes Hills, California: A 60th Anniversary Revisit to Commemorate 1946 Publication of U. S. Geological Survey Professional Paper 207: Pacific Section SEPM book 103, p. 51-72.
Californiacoastline.org, <http://www.californiacoastline.org>
Cherven, V.B., Russell, P.W., 1987. Glaucophane-rich lithic sandstone at Point Fermin, California. In: Fischer, P.J. (Ed.), Geology of the Palos Verdes Peninsula and San Pedro Bay. Pacific Section, Society of Economic Paleontologists and Mineralogists, Los Angeles, CA, pp. 53–56.
Ingersoll, R. V., Bullard, T. F, Ford, R. L., Grimm, J. P., Pickle, J. D., and Sares, S. W, 1984. The effect of grain size on detrital modes: a test of the Gazzi-Dickinson point-counting method: Journal of Sedimentary Petrology, v. 54, p. 103-116.
Russell, P.W., 1987. Point Fermin submarine fan: A small late middle Miocene age fan within the Monterey Formation. In: Fischer, P.J.(Ed.), Geology of the Palos Verdes Peninsula and San Pedro Bay. Pacific Section, Society of Economic Paleontologists and Mineralogists, Los Angeles, CA, p. 31–46.
Sloan, J. R.., 1987. Age and Paleooceanography of the Point Fermin fan complex. In: Fischer, P.J.(Ed.), Geology of the Palos Verdes Peninsula and San Pedro Bay. Pacific Section, Society of Economic Paleontologists and Mineralogists, Los Angeles, CA, p. 47–52.
Spotts, J. H., 1964, Grain orientation and imbrication in Mioce:1e turbidity current
sandstones: California: Journal of Sedimentary Petrology, v. 34, p. 229-253
Spotts, J. H, and Silverman, S. R, 1966, Organic dolomite from Point Fermin California: The American Mineralogist, v. 51, p. 1144-1155.