## Slide 1: Diagenetic and Compositional Controls of Wettability in Siliceous Sedimentary Rocks, Monterey Formation, California
Kristina Hill
MARS Project
CSULB 2014
Committee:
Dr. Richard J. Behl
Dr. Matthew Becker
Dr. Hilario Camacho

## Slide 2: Overview
Introduction
  Review of Wettability
  Importance of Project
Experiment Objective
Methods
Results
Preliminary Discussion

## Slide 3: Introduction
Wettability is …
  The relative affinity between a surface and a fluid.
And is affected by
  temperature
  fluid chemistry
  rock mineralogy
  Secondary constituents
(Abdullah, et al., 2007, top & bottom)
Notes: Figure 1. Contact angle. An oil drop (green) surrounded by water (blue) on a water-wet surface (left) forms a bead. The contact angle θ is approximately zero. On an oil-wet surface (right), the drop spreads, resulting in a contact angle of about 180°. An intermediate-wet surface (center) also forms a bead, but the contact angle comes from a force balance among the interfacial tension terms, which are γso and γsw for the surface-oil and surface-water terms, respectively, and γow for the oil-water term. (Abdullah, et al., 2007)
Wettability is …
  The relative affinity between a surface and a fluid.
  demonstrated in a fluids propensity to spread or bead on a surface
  the product of the hydrostatic intermolecular interactions between the rocks and a fluid phase (Hirasaki, 1991, as cited in Civan, 2004)
Wettability affects
  location, flow and fluid distribution in a reservoir (Karabakal and Bagci, 2003).
And is affected by
  temperature
  fluid chemistry
  rock mineralogy
  Secondary, or non-matrix rock constituents (clay, carbonate, clastics, etc.)
Wettability in the Monterey Formation must be better understood in order to produce at maximum potential

## Slide 4: Introduction
Importance of project
  Extensive reserves in Monterey
  Still highly underdeveloped
  Low porosity and permeability (quartz and opal-CT phase)
    high surface area to volume ratio of reservoir fluids
    More interaction between fluid and rock surface
  Silica diagenesis expels water from crystal structure
    may impact hydrocarbon distribution
Notes:   The Monterey is currently estimated to hold 64%, or 15.42 billion barrels of recoverable shale oil in the U.S. (Intek, 2011). (Need to update this data – now considered untrustworthy)

## Slide 5: Objective
Identify and quantify alteration in wettability of siliceous rocks due to silica diagenesis
Characterize and Quantify alteration in siliceous rock wettability due to abundance of detritus

## Slide 6: Methods
Approach
    Goals
      Measure wettability on actual reservoir samples of each silica phase; opal-A, opal-CT and quartz
      Eliminate permeability and porosity geometry differences between phases as variables
      Eliminate reservoir fluid chemistry as a variable
    Limitations:
      Ultra low permeability opal-CT and quartz phase porcelanites and cherts
      Porous core samples

## Slide 7: Methods
Wettability Measurements
    Oil/Water Imbibition Rate
    Contact Angle
Rock Composition
    XRD/Elemental Analysis
    FTIR
Characterize & Quantify Variable Correlations
    Data trends
    Multivariate Statistics

## Slide 8: Methods
Imbibition Tests
  Distilled H2O
  Castrol HD40
  69 Core Samples
  Controls:
    Sample density (wt, size & compaction)
    Fluid drop size
Contact Angle Tests
  Distilled H2O
  Castrol HD40
  6 Chert samples (opal CT & quartz)
  3 non-biogenic mineral samples
    one from each phase

## Slide 9: Results
Data Collected:
  Contact Angle Measurements
  Imbibition Tests
  XRD
  Elemental Analysis
Basic Trend Analysis
  Silica phase vs. wettability
  % Detritus vs. wettability

## Slide 10: Results - XRD

## Slide 11: Results – Elemental Analysis
OXIDES
ELEMENTAL ABUNDANCES
By ActLabs
Notes: 78 Samples

## Slide 12: Results – Elemental Analysis vs Imbibition Rates & Contact Angles

## Slide 13: Results – Quartz Trends
Weak Water trends
Stronger Oil Trends
Notes: *Silica is calculated from Isaac’s (1980) dissertation, where
Si = SiO2 – (3.5*Al2O3) to distinguish biogenic & diagenetic silica from detrital quartz
This value is then normalized by dividing the bio & dia silica by the total combined bio & dia silica and detritus (also calculated from Isaac’s equation, Detritus = 5.6*Al2O3)

## Slide 14: Silica Phase vs. Oil Contact Angle
Chart: Detritus vs Oil Contact Angle
| 8.86916666666667
Hyalite | 0.0092669
Qtz-1 | 0.018833
Qtz-2 | 0.040997
Qtz-3 | 0.041489
CT-1 | 0.029119
CT-2 | 0.040274
CT-3 | 0.05211
CT-4 | 0.013818
IC-Opal | 0.0048516
Chart: Detritus vs Oil Contact Angle
| 8.86916666666667
Hyalite | 0.0092669
Qtz | 0.018833 | 0.040997 | 0.041489
Opal-CT | 0.029119 | 0.040274 | 0.05211 | 0.013818 | 0.0048516
Notes: Maybe Qtz has the opposite trend as CT?

## Slide 15: Future Work
FTIR
  Quantify the ratio of biogenic & diagenetic silica to detritus
Multivariate Analysis
  Characterize & quantify relationships between wettability and other compositional variables

## Slide 16: Special Thanks to:
Occidental Petroleum and Aera Energy for core sample donation
Dr. Varenka Lorenzi and staff of the IIRMES Lab at CSULB for Soxhlet extraction materials, instruction & supervision
Dr. Young Shon, CSULB Chemistry Dept., for CAM-101 Tensiometer use

## Slide 17: References
F. Civan, Temperature dependence of wettability related rock properties correlated by the Arrhenius equation, Petrophysics (Houston, Tex.), August 2004, 45(4):350-362
U. Karabakal and S. Bagci, Determination of wettability and its effect on waterflood performance in limestone medium, Energy & Fuels, April 2004, 18(2):438-449
Isaacs, Caroline M., 1980,Diagenesis in the Monterey Formation examined laterally along the coast near Santa Barbara, California, USGS Open-File Report: 80-606