## Slide 1
Compositional and Diagenetic Controls of Hardness; Implications for Fracture Development
By: Ryan Weller
Committee: Richard Behl, Jon Schwalbach, and Tom Kelty
MARS Project, CSULB, Geological Sciences
Upper Monterey Formation, Belridge Oil Field, San Joaquin Valley, California

## Slide 2: Monterey Formation - Diagenesis
Highly contrasting physical properties via compositional and diagenetic variability

## Slide 3: Mechanical Stratigraphy
Composition + diagenesis + bed thickness + structural position =
Varied fracture style and density (Mechanical Stratigraphy)
Gross, 1995
Arroyo Burro Beach, CA
Notes: Great physical contrasts lead to heterogeneous and anisotropic mechanics
Outcrops show BOLD and Distinct Fracture stratigraphy based on comp, bed, position..

## Slide 4: Hypothesis and Goals
Mechanical properties are strongly influenced by composition and silica diagenesis.
Test a wide range of subsurface core at a high resolution to quantify:
Composition
Diagenesis
Physical properties (porosity)
Mechanical properties (rebound hardness and UCS)

## Slide 5: Methods – Belridge Oilfield
CT-QTZ
A-CT
Notes: Ccore and well data from Aera Energy at the Belridge Oilfield,
used well logs to identify diagenetic transition zones by density and porosity shifts
Selected core samples from correlative horizons at different burial depths.
4 Wells (over 80 ft of core)
Compositionally diverse
Diagenetically contrasting
Stratigraphically similar horizons
Identify diagenetic shifts in wireline
The most interesting core we were excited to consider were two cored wells that test the same quartz phase interval at the top of the McDonald at 6k and 12k feet.

## Slide 6: Methods – XRF Scanning
1 cm2 resolution
Qualitative Elemental Analysis of Al, Si, P, S, Cl, K, Ca, Ti, Cr, Mn, and Fe
Over 27,500 XRF data points
Clean
Scan
Results
Si
Al
Ca
K
X-Ray Fluorescence
Notes: Cleaned the 2/3 sections that were often filthy with this crust of degraded surface and mineral precip
Scanned at Scripps Institution of Oceanography at 1cm

## Slide 7: Silica:Detritus Definition
XRF Corrected for elemental fluorescence yield and normalized to total counts
Inductively Coupled Plasma – Mass Spectrometry (ICP-MS)
  25 samples analyzed 8 elemental oxides – correlated to XRF
Covert Oxides to Normalize Si:Detritus (Isaacs, 1980)
  Biogenic and Diagenetic Silica % = SiO2 – (3.5x Al2O3)
  Detritus % = 5.6 x Al2O3

## Slide 8: Methods – Leeb Hardness (HLD)
Proceq Piccolo Rebound Hardness tester
12,500 total measurement
Average of 5-7 of the highest values w/ suspected errors removed
  1,546 HLD data points
6.5 inches
Notes: Leeb hardness testing
NOT MOHs scale of hardness – like glass plates, pocket knives and pennies
But a fast and precise Non Destructive testing
Tungsten carbide probe, sprung against the surface
Carries a relationship to Youngs Modulus and calibrated conversion to UCS

## Slide 9: Hardness Results
Length 3.2ft
Increasing Silica = Increasing Hardness
Significant trends
Limited Opal-A results
Notes: Mixed A-CT = 13% opal-A and 87% opal-CT

## Slide 10: Results – Hardness in Depth
Tremendous variance
Significant overlap
Stepwise shifts with diagenesis
12k’ Quartz hardening

## Slide 11: Stepwise Hardening with Diagenesis
Stepwise Shifts in Hardness
Not Gradual Sediment Compaction
Notes: NOT a standard burial compaction - Important because no geomechanical equations are built to handle complex diagenesis and high porosity

## Slide 12: Controls - Burial Compaction
Opal-CT resistance to burial compaction
  Rigid and relatively strong rock with micro-crystalline fabric
No offset = no compaction
Notes: 40% step through opal-CT with no increase in HLD

## Slide 13: Controls – Porosity and Composition
Trend -> Higher porosity in silica-rich rocks
z
Porosity (%)
Notes: Estimations of mechanical properties or brittleness is often tied to porosity.
This chart shows standard and unusual behavior of the relationship between porosity and composition.

## Slide 14: Controls
Sample Group | Log Trend of mean HLD points | Correlation of determination (R2)
opal-A | HLD=-0.55 x (% Si) + 346.91 | 0.33
mixed opal-A+CT | HLD= 1.99 x (% Si) + 408.24 | 0.71
opal-CT | HLD= 3.88 x (% Si) + 356.33 | 0.97
6k’-quartz | HLD= 1.86 x (% Si) + 517.38 | 0.83
12k’-quartz | HLD= 2.18 x (% Si) + 655.86 | 0.97
Composition
Variable Porosity Loss
Silica Diagenesis
Clay Diagenesis
Catagenesis
Variable Physical Compaction

## Slide 15: Controls – Composition and Diagenesis
Notes: Rocks of similar composition are in different silica phases and what aspects of lithologies are becoming harder at variable rates
Catagenesis, OM
I/S

## Slide 16: Hardness Variability and Controls
Composition
Variable Porosity Loss
Silica Diagenesis
Clay Diagenesis
Catagenesis
Variable Physical Compaction
Notes: 800-1000’ opal-A sample, 1900’ mixed A&CT samples, 2-4000’ opal-CT samples, and quartz phase samples at 6 and 12 thousand feet.

## Slide 17: Comparison
Notes: Aggregated data from 6 other NA Shale plays, broken into lithotypes
Note that in the Monterey, hardness is distributed by composition, and this is similar in other shales
Detritus rich are weakest, this includes ash beds that have altered to bentonite clay.
Carbonate-rich lithotypes - less hard than CT and Quartz phase Monterey, both less than 7,000’ and thermally immature!
Hardest are highly siliceous and deepest buried (GAS)

## Slide 18: Applications
Drilling Efficiently
  ROP
  AZI and INC drift
Fracture Closure
  Self arresting (breccia)
  Proppant embedment
Wellbore stability
  Casing shear
  Borehole collapse
Fracturability or Frac Design
  Location and extent of induced or natural fractures
  Barriers to
New Play Concepts
  Duel permeability targets

## Slide 19: Implications - Failure Criteria

## Slide 20: 12’k-Quartz
>11,000’ = Higher strength and Heterogeneity
Deep Quartz
  Potentially Very Hard (Fast)… Too Hard?
  Clay-poor (silica-rich) are hardest, fastest, lowest por.
  Generic mineralogical BI is not appropriate
    Highest clay & kerogen-rich rocks are still really hard!
?
Notes: Monterey is TOO Strong at extreme end
Compared to many other unconventional shales, they are much harder, so Opal-CT is possibly more brittle at shallower depths; but also 12k’-quartz is much harder, maybe too hard?

## Slide 21: HLD to Wireline Resolution

## Slide 22: HLD to Wireline Resolution

## Slide 23: Summary
Strong trends with composition
  Can be correlated to spectral GR
  Inconclusive Opal-A
Quantified Diagenetic hardening
  Opal-A to mixed A+CT is greatest
  Opal-CT resistance to compaction
  Opal-CT to Quartz is lesser
Porosity is too complex for simple geomechanical guidance
Distinct character of deep and cemented quartz phase rocks

## Slide 24: Summary
Hardness by
  Detritus Content
  Silica Mineralogy
  Burial Depth / Thermal Maturity
Measurable and mappable
  GR correlation
  Play Concept and Exploration Potential
Historical strength and basin modeling
Fundamental differences to other shale plays
Future Work
Illite/Smectite
Pure cherts & diatomite
Pressure and temperature
Match to drilling parameters
SEM and thin section analysis
Natural fracture timing
Texture, fabric, micro-porosity
Dolomite and pyrite
Ideas?

## Slide 25: Questions and Discussion
Thanks to the MARS Project supporters for data, core access, the Proceq rebound hardness tester, and guidance.
Thanks to my committee and CSULB colleagues.
Near Point Sal Beach, CA. Jointed opal-CT porcelanite and unfractured siliceous mudstone; quarter (25₵) for scale.

## Slide 27: Unconfined Compressive Strength - UCS
Stress loading to brittle strain (brittle failure)
Close relationship to elasticity (Young’s Modulus)
AKA uniaxial compressive strength
Lee et al. (2014) added shale to established conversion: rebound hardness –> UCS
www.geocomp.com

## Slide 28: Rebound Hardness to UCS conversion
Applied Lee et al. (2014) literature trend line to Monterey Formation HLD
Modified from Lee et al. (2014)
Measured diatomite UCS (800-1485psi) (Strickland 1985, Hansen and Purcell 1989, Bruno and Bovberg 1992)
Measured CT UCS (4,000-7,500psi)
Measured QTZ 5k’ UCS (8,000- 13,000 psi) (TeraTek)
Measured QTZ 12k’ UCS (18,200 – 30,300psi) (Core Labs)
Notes: Monterey lithologies have a range of rock strengths that span most sedimentary and igneous rock types.
If your reservoir was mixed granite, limestone and shale, you would definitely take rock mechanics into serious consideration.

## Slide 29: USC (MPA vs PSI)

## Slide 30: Comparably Higher Rock Strength
*Calculated UCS
Marcellus Shale
Bakken (Mid)
Barnett
Haynesville
Eagle Ford
Muderrong Shale
Notes: A 15,000psi variance in CT and quartz by composition alone
The Marcellus the Austin Chalk, the Eagle Ford….
2 Things (these weak rocks are FRACTURABLE) (and most of our Monterey rocks are SHALLOWER, with less confining pressure)

## Slide 31: Hardness Results
Good agreement with compositional variance
High resolution hardness in compositional groups
Length 3.2ft
Biogenic or diagenetic Silica

## Slide 32: Silica Diagenesis + Nomenclature